## Slide 1
https://newatlas.com/military/ursa-major-hypersonic-engine-hotfire-tests/
Analysis done using dynamight
Primary Challenge:
  Engine hotfires need to be processed regularly
  10+ total engines, many tests, 100k Hz
  Many accelerometers (Typically ~15 axes per engine)
  Verify in family; verify past results in family
  Very manual process and many other things to do
Requirement: Setup process and give to new grads to run as tests come in
Secondary Req: Predict component responses in other locations on vehicle and verify appropriately margined
Process Engine Data
Data is per aircraft takeoff example
https://endaq.com/pages/free-vibration-analysis-files
Pre-Test

## Slide 2
Step 1: Look at baseline engine data
  Mean is biased by non-data; large transient
  Need to deal with transients
  Start by removing pre-test
Quick Look
Pre-Test

## Slide 3
Takeoff transient is 28s / 188s = 15%
Engine transient is 3-5s / 180s = 2-3%
Shock event processing not addressed here
Log Mean barely changed
Remove Pre-Test

## Slide 4
Core signal is largely ergodic and stationary
  Ideal signal
  No filtering required
Log Mean is 50/50 (unmargined) ASD curve
Remove Transient
Log Mean

## Slide 5
Calculate Log Mean as previously on whole signal
Filter data below Log Mean (set to NaN)
Calculate Log Mean based on new data (log mean filtered)
Slightly conservative if you remove pre-test
Filter Low Data and Reprocess

## Slide 6
Repeat process but with same full data set
  Slightly conservative, but in the noise
  Actual transient was ~1/5th as long
Repeat for entire family bounding to get P50/50
Run SEA analysis (didn’t do this step)
Lesson Learned:
  Not having established process & tools made large datasets difficult to process
    Simple tools go a long way
  Being slightly conservative lets you quickly identify issues
Do it Faster

## Slide 7
Convolve sub-components responses using Lab Data
  Time Domain Convolution is Freq Domain Multiplication
Component level Prediction/Testing
https://www.halthass.co.nz/lab-services/vibration-and-shock-testing

## Slide 8
Convolve Signals
  Acceptance test performed at P95/50
    Add 4.9 dB to go from P50/50 to P95/50
    Add 5.9 dB uncertainty for first flight (Table B.1.1-1)
Additional mode characterized
  Strong impact on FTS electrical component
  2x decrease in PSD amplitude would correct issue (minimal damping)
  Very localized mode (shifting mode would fix problem)
  Loosely tightened grommets fixed issue (not for flight)
  Proposed low profile damper config change
Lessons Learned: Breaking down components and running individual sine sweeps allows you to understand what you’re seeing during random vibe
Final Predictions & Modification
Critical Mode
https://explorers.larc.nasa.gov/2019APSMEX/MO/pdf_files/SMC-S-016_05SEP2014.pdf